## Slide 1: SMART INDIA HACKATHON 2026 Problem Statement ID: 26052
AI/ML-Enabled Adaptive Noise Cancellation for Defence Communication
Theme: Miscellaneous
PS Category: Hardware
Team ID: [YOUR TEAM ID]
Team Name: [YOUR TEAM NAME]
Noisy Env.
AI Processor
Clear Speech

## Slide 2
AI-Powered Adaptive Noise Suppression for Defence Communication
Proposed Solution: A causal, stateful deep-learning speech enhancement system that suppresses stationary, non-stationary and impulsive noise while preserving speech information for low-latency defence communication.
Key Innovation:
• Stateful Polar-LSTM maintains temporal context across audio frames.
• Predicts magnitude + phase corrections instead of magnitude alone.
• Causal processing enables real-time streaming without future audio.
• Compact ~1.45M-parameter model for edge deployment.
Userflow Diagram:
Noisy Speech
Causal STFT
Polar-LSTM
Spectral Mask
Causal iSTFT
Enhanced Speech

## Slide 3
Architecture & Technology Stack
Signal Processing:
• 16 kHz mono, 16 ms frames
• 512 FFT size, 256 hop size (257 bins)
• Causal STFT / iSTFT
AI Model (Stateful Polar-LSTM):
• Explicit recurrent hidden + cell states
• Input: 514 features (Real + Imag)
• Output: Mag mask [0, 2], Phase [-π, π]
• 1,448,962 parameters
Training / Evaluation Data:
• LibriSpeech, MUSAN, ESC-50, UrbanSound8K
• IoBT Gunfire Audio Dataset (Defence Domain)
Implementation Pipeline:
• Python + PyTorch -> Raspberry Pi 5 -> Edge Streaming
Technical Architecture Flow:
Mic / Audio
16 kHz Stream
Causal STFT
(257 bins)
Polar-LSTM
(Stateful)
Mag + Phase
Mask
Causal iSTFT
Enhanced
Audio

## Slide 4: Edge Feasibility + Experimental Validation
Raspberry Pi 5 Edge Benchmark (3,600 frames):
• Deadline misses: 0
• p95 processing time: 5.7 ms (Limit: 16 ms)
• Max processing time: 11.7 ms
• Peak temperature: 49.4C | RAM usage: ~258 MB | Throttling: None
Canonical Model Validation (590 mixtures):
• SI-SDR Improvement: +0.335 dB (p = 3.49 x 10^-28)
• SNR Improvement: +0.129 dB (p = 0.00441)
• Statistically significant changes also observed in STOI and PESQ
Challenges -> Mitigation:
• Non-stationary noise -> Stateful temporal modeling
• Impulsive/gunfire noise -> Defence-domain training data
• Phase distortion -> Polar complex masking
PROTOTYPE STATUS:
AI model + Raspberry Pi edge pipeline validated.
Physical microphone/acoustic-loop validation is the next prototype stage.

## Slide 5: Impact on Defence Communication
Primary Target Applications:
• Tactical Communication: Clearer voice in high-noise operational environments.
• Aviation / Helicopter Crews: Speech enhancement under continuous engine noise.
• Armoured & Military Vehicles: Suppression of engine and impulsive noise.
• Field Communication Systems: Low-latency processing directly at the edge.
Key Benefits:
1. Improved Speech Intelligibility without cloud dependency.
2. Low-Latency Edge Processing for real-time operation.
3. Adaptive Noise Handling tracking temporal changes.
4. Defence-Domain Robustness using gunfire data.
5. Local & Portable execution on compact computing hardware.
Potential Extensions: Emergency Response -> Industrial Safety -> Aviation -> Disaster Communication

## Slide 6: Research, Datasets & Technical References
Datasets Utilized:
• LibriSpeech (clean speech)
• MUSAN, ESC-50, UrbanSound8K (environmental noise)
• IoBT Gunfire Audio Dataset (defence-domain firearm recordings - DOI: 10.5281/zenodo.6836031)
Technical Foundations:
• Causal real-time signal processing (STFT / iSTFT)
• Long Short-Term Memory networks (LSTM)
• Complex spectral masking & Objective metrics (SI-SDR, PESQ)
• PyTorch edge inference on Raspberry Pi 5
Core Research Direction:
Deep-learning speech enhancement + complex-domain spectral processing + recurrent temporal modeling + edge inference.